## Slide 1: Unit 3: Coordinate Reference System

## Slide 2: Coordinate Reference System
Useful terms: Geoid, Ellipsoid, Datum, EPSG...
Coordinate systems: Geographic Coordinate system, Projected Coordinate system
VN-2000 - WGS84 CRS transfer for each province in AutoCAD Civil 3D

## Slide 3: Coordinate Reference System
Earth Surface: too complex to be useful as a reference for measurement.
Geoid, Ellipsoid: approximation of the surface of the earth

## Slide 4
Geoid: The surface of the earth's gravity field, which is approximately the same as mean sea level.
  The geoid is a representation of the surface of the earth that it would assume, if the sea covered the earth.
  Perpendicular to the direction of gravity pull
  The mass of the Earth is not uniform + the magnitude of gravity varies  the shape of the geoid is irregular.
Coordinate Reference System

## Slide 5: Coordinate Reference System
Ellipsoid (Spheroid): To simplify the Geoid model
  Three-dimensional shape created from a two-dimensional ellipse
  Various spheroids or ellipsoids have been devised: Clarke_1866, GRS_1980, WGS_1984

## Slide 6: Coordinate Reference System
WGS84 Ellipsoid (World Geodetic System 1984):
  Origin is at the Earth’s center of mass (geocentric)
  Used for the NAVSTAR GPS satellites
Parameter | Notation | Value
Semi-major Axis | a | 6378137.0 m
Semi-minor Axis | b | ≈ 6 356 752.314 245 m
Flattening Factor of the Earth | 1/f (f = (a-b)/a) | 298.257223563
Nominal Mean Angular Velocity | ω | 7292115 10-11 rad/s
Geocentric Gravitational Constant | GM | 3986004.418 108 m3/s

## Slide 7: Coordinate Reference System
Datum:
  Built on top of the selected ellipsoid
  Consists of a series of numbers that define the shape and size of the ellipsoid and it's orientation in space
  A datum is chosen to give the best possible fit to the true shape of the Earth.
  There are a large number of datums in use

## Slide 8: Coordinate Reference System
Vietnam 2000 Datum:
Ellipsoid: WGS 84
Prime meridian: Greenwich
Degree from Greenwich: 0
Data source: OGP
Information source: General Director of Land Administration.
Revision date: 2011-01-25
Scope: Geodetic survey, topographic mapping, engineering survey.
Remarks: Replaces Hanoi 1972.
Area of use: Vietnam - onshore.

## Slide 9: Coordinate Reference System
Coordinate Systems: Geographic vs. Projected
Geographic Coordinate Systems (GCS)
    Location measured from curved surface of the earth
    Measurement units latitude and longitude
      Degrees-minutes-seconds (DMS)
      Decimal degrees (DD) or radians (rad)
Projected Coordinate Systems (PCS)
    Flat surface
    Units can be in meters, feet, inches
    Distortions will occur, except for very fine scale maps

## Slide 10: Map Projection
Map projection:
  The Earth is curved and maps are flat
  A map projection uses mathematical formulas to relate spherical coordinates on the globe to flat, planar coordinates.
  Wide variety of projections possible
  Each projection will create a different type of distortion (shape, area, distance, or direction)
  One map projection might be used for large-scale data in a limited area, while another is used for a small-scale map of the world

## Slide 11: Map Projection
Map projection:
  Sets of mathematical equations that convert coordinates from one system to another
input output
unprojected projected
angles (lat/long) Cartesian coordinates

## Slide 12: Map Projection
Classification of Map projections:

## Slide 13: Map Projection
Classification of Map projections:

## Slide 14: Map Projection
Classification of Map projections:
CONIC: Alber Projection
CYLINDRICAL: Mercator PROJECTION
Azimuthal: LAMBERT AZIMUTHAL
EQUAL-AREA PROJECTION

## Slide 15: Map Projection
Map projections:
  Over 200 of Map projections (https://map-projections.net/imglist.php)

## Slide 16: Map Projection
Map projections:
  Each projection preserves a particular relationship or characteristic:
    Equal-Area: preserves the size of feature
    Conformal: preserves the shape of feature (UTM)
    Equidistant: preserves the distance between two features
    True Direction (Azimuthal): preserves the compass direction between 2 features (great circle distance)
  A map cannot be at the same time equal-area, conformal and/ or equidistant
  A Map projection is to be chosen based on the needs

## Slide 17: Map Projection
Map projections:

## Slide 18: Map Projection
UTM (Universal Transverse Mercator)
  The UTM projection is an adaptation of the standard Mercator projection which flips the cylinder 90 degrees (transverse).
  The UTM projection flattens the sphere 60 times by shifting the cylinder central meridian 6° for each zone.
  The UTM is horrible for small-scale (less-detailed) maps like world atlases and perfect for mapping narrow regions

## Slide 19: UTM Map projection:
UTM Map projection:
  UTM divides the earth into 60 zones each 6 degrees of longitude wide.

## Slide 20: Coordinate Reference System
UTM Map projection:
  The UTM system divides the Earth into 60 zones, each 6° of longitude in width.
  A square grid is superimposed on each zone. It's aligned so that vertical grid lines are parallel to the center of the zone (called the central meridian)
  A single grid zone measures about 20,000km tall and only about 700km wide.
  UTM grid coordinates are expressed as a distance in meters to the east, referred to as the "easting", and a distance in meters to the north, referred to as the "northing".

## Slide 21: Coordinate Reference System
False easting is a linear value applied to the origin of the x coordinates.
False northing is a linear value applied to the origin of the y coordinates.
 False easting and northing values are usually applied to ensure that all x and y values are positive.

## Slide 22: Coordinate Reference System
False Easting:
  False easting (500,000) is given to the central meridian in each zone to prevent the use of negative values.
False Northing
  False Northing (10,0000,000) are added to the South of the Equator to avoid negative values

## Slide 23: UTM Projection
Scale factor:
  For UTM (6 degree zones), the central meridian (CM) has a scale factor of 0.9996
  True Distance (m) = Map Distance ÷ scale factor
  The scale factor reduces the overall distortion of the projection in the area of interest.

## Slide 24: Coordinate Reference System
EPSG.io: Coordinate Systems Worldwide
  VN-2000:
+proj=longlat +ellps=WGS84 +towgs84=-192.873,-39.382,-111.202,-0.00205,-0.0005,0.00335,0.0188 +no_defs

## Slide 25: Coordinate Reference System

## Slide 26: Coordinate Reference System

## Slide 27: Coordinate Reference System

## Slide 28
Create Coordinate system
  Choose Planning and Analysis Workspace
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 29
Create Coordinate system
  In Map Setup  Create Coordinate System Definition
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 30
Create Coordinate system
  Start with a coordinate system
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 31
Create Coordinate system
  Create a new Coordinate System with Projected type
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 32
Create Coordinate system
  Input parameters:
    Code: Appropriate Name
    Description: Appropriate Desc
    Source: Author’s name
    Unit: Meter
    Available Categories: Vietnam Add
    Geodetic  Select Vietnam 2000
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 33
Create Coordinate system
  Input parameters:
    Central medidian:105 (for Bac Lieu Province)
    False easting: 500000
    Scale reduction: 0.9999 (for Cadastral map with 3 degrees zone width of)
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 34
Create Coordinate system
  Input parameters:
    Min Longitude: 102
    Max longitude: 117
    Min Latitude: 0
    Max Latitude: 90
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 35
Create Coordinate system
  Finish!
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 36
Create Coordinate system
  Check again in the Library
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 37
Create Coordinate system for other Provinces based on VN200-BacLieu
  Go to Library and Search BacLieu
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 38
Create Coordinate system for other Provinces based on VN200-BacLieu
  Go to Library and Search BacLieu: Duplicate and Edit
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 39
Create Coordinate system for other Provinces based on VN200-BacLieu
  Change Central Meridian for each Province
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 40
Create Coordinate system for other Provinces based on VN200-BacLieu
  Change Central Meridian for each Province
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 41
Assign CRS for VN-2000 AutoCAD file:
  In Map Setup menu  Assign
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 42
Check the result: In Geolocation menu  Choose Basemap  Done
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 43
VN-2000 to WGS84 in MicroStation V8i
VN-2000 to WGS84 in Microstation
Download VN2000.dty from https://github.com/hcmgis/QGIS-Training/blob/master/VN2000.dty
Menu\Workspace\Configuration  All (Alphabetial)
New:
  Variable: MS_GEOCOORDINATE_USERLIBRARIES
  Value: VN2000.dty file path (D:\VN2000.dty)
  Restart MicroStation

## Slide 44
VN-2000 to WGS84 in MicroStation V8i
VN-2000 to WGS84 in Microstation
  Tool\Geographic\Select Geographic Coordinate System  From library
  Select appropriate VN2000 projection for each province
  Export to KML and open in Google Earth

## Slide 45
In QGIS: Settings Custom projection
VN-2000 to WGS84 in QGIS
Bình Thuận Province:
+proj=tmerc +lat_0=0 +lon_0=108.5 +k=0.9999 +x_0=500000 +y_0=0 +ellps=WGS84 +towgs84=-191.9044129,-39.30318279,-111.45032835,-0.00928836, 0.01975479, -0.004274, 0.252906278 +units=m +no_defs

## Slide 46
“On the fly” projection:
  Like putting on a pair of glasses
  You see the map differently, but the data have not changed
VN-2000 to WGS84 in AutoCAD Civil 3D

## Slide 47: Keep Calm and enjoy Learning!
https://hcmgis.vn
HCMGIS – GIS for the City, GIS for the Community